## Slide 1
Classification used for health risk estimate interpretation and map visualization
CHRONIC RISK
CANCER RISK
Health risk estimate
Note: The same classification used for Hazard Index (HI)

## Slide 2
Interpretation of health risk estimates in map and table form was performed for all administrative units of the Slovak Republic – municipalities, districts and regions
District/Region | CAs | HQadult | Chronic risk | ELCR | Cancer risk
Bratislavský | 0.0025 | 2.32E-01 | 1 | 1.04E-04 | 4
Bratislava I | 0.0011 | 1.01E-01 | 1 | 4.55E-05 | 1-3
Bratislava II | 0.0009 | 8.68E-02 | 1 | 3.90E-05 | 1-3
Bratislava III | 0.0015 | 1.41E-01 | 1 | 6.36E-05 | 1-3
Bratislava IV | 0.0012 | 1.12E-01 | 1 | 5.02E-05 | 1-3
Bratislava V | 0.0009 | 8.14E-02 | 1 | 3.66E-05 | 1-3
Malacky | 0.0031 | 2.89E-01 | 1 | 1.30E-04 | 4
Pezinok | 0.0024 | 2.26E-01 | 1 | 1.02E-04 | 4
Senec | 0.0022 | 2.05E-01 | 1 | 9.23E-05 | 1-3
Trnavský | 0.0012 | 1.11E-01 | 1 | 5.00E-05 | 1-3
Dunajská Streda | 0.0012 | 1.12E-01 | 1 | 5.04E-05 | 1-3
Galanta | 0.0014 | 1.36E-01 | 1 | 6.13E-05 | 1-3
Hlohovec | 0.0007 | 6.71E-02 | 1 | 3.02E-05 | 1-3
Piešťany | 0.0008 | 7.16E-02 | 1 | 3.22E-05 | 1-3
Senica | 0.0015 | 1.40E-01 | 1 | 6.30E-05 | 1-3
Skalica | 0.0015 | 1.38E-01 | 1 | 6.21E-05 | 1-3
Trnava | 0.0008 | 8.09E-02 | 1 | 3.64E-05 | 1-3
Trenčiansky | 0.0044 | 4.22E-01 | 1 | 1.90E-04 | 4
Bánovce nad Bebravou | 0.0011 | 9.99E-02 | 1 | 4.49E-05 | 1-3
Example for arsenic in groundwater in Slovak districts / regions
All results are available on the website www.geology.sk/geohealth
Total No. of evaluated administrative units:
2883 municipalities,
79 districts,
8 regions.

## Slide 3
Health risk estimate for chronic disease occurrence due to groundwater ingestion by adult population of the Slovak Republic – MUNICIPALITIES (As, Ba, Cd, Cu, F, Hg, Mn, NO3, Pb, Sb, Se, Zn) – expressed in the form of maximum of hazard quotient (HQ)
Chronic risk estimate for groundwater contamination
Main results: chronic risk was documented in 17 municipalities, arsenic and antimony were defined to share the significant part of total risk level

## Slide 4
Health risk estimate for chronic disease occurrence due to groundwater ingestion by adult population of the Slovak Republic – MUNICIPALITIES (As, Ba, Cd, Cu, F, Hg, Mn, NO3, Pb, Sb, Se, Zn)
Main results: high chronic risk was documented in 20 municipalities, arsenic and antimony were defined to share the significant part of total risk level, the summary effect of calculation of hazard index is reflecting mainly in classification of municipalities in lowland areas (Suthern part of the Slovak Republic) into category of medium chronic risk
Chronic risk estimate for groundwater contamination

## Slide 5
Health risk estimate for chronic disease occurrence due to groundwater ingestion by adult population of the Slovak Republic – MUNICIPALITIES
Main results: medium to high chronic risk was documented mainly in highly contaminated areas with geogenic or geogenic-anthropogenic sources of contamination (ore deposit and mineralized occurrences, associated historical mining activities ), medical-geochemical research made in the region of Spišsko-gemerské rudohorie revealed the negative impact of high As groundwater contents and health status of inhabitants.
Chronic risk estimate for groundwater contamination

## Slide 6
Health risk estimate for chronic disease occurrence due to groundwater ingestion by adult population of the Slovak Republic – MUNICIPALITIES
Main results: medium to high chronic risk was documented mainly in highly contaminated areas with geogenic or geogenic-anthropogenic sources of contamination (ore deposit and mineralized occurrences), medical-geochemical research made in the region of Spišsko-gemerské rudohorie revealed the negative impact of high Sb groundwater contents and health status of inhabitants.
Chronic risk estimate for groundwater contamination

## Slide 7
Health risk estimate for chronic disease occurrence due to groundwater ingestion by adult population of the Slovak Republic – MUNICIPALITIES
Example of health risk estimate for nitrate groundwater contents, low risk is documented in lowland areas with agriculuture land-use.
Chronic risk estimate for groundwater contamination

## Slide 8
Health risk estimate for chronic disease occurrence due to soil ingestion by child population of the Slovak Republic – MUNICIPALITIES (As, B, Ba, Be, Cd, Cu, F, Hg, Mn, Mo, Ni, Pb, Sb, Se, Zn) – expressed in the form of maximum of hazard quotient (HQ)
Chronic risk estimate for soil contamination
Main results: the majority of Slovak municipalities were classified into the category of no or low chronic risk.

## Slide 9
Health risk estimate for chronic disease occurrence due to soil ingestion by child population of the Slovak Republic – MUNICIPALITIES (As, B, Ba, Be, Cd, Cu, F, Hg, Mn, Mo, Ni, Pb, Sb, Se, Zn)
Main results: medium to high chronic risk was documented in 26 municipalities, arsenic, antimony and lead were defined to share the main part of total risk level, the territory of the Slovak Republic is from the point of view of soil contamination by other evaluated contaminants at no risk.
Chronic risk estimate for soil contamination

## Slide 10
Health risk estimate for chronic disease occurrence due to soil ingestion by child population of the Slovak Republic – MUNICIPALITIES
Main results: medium risk levels were documented only in 10 municipalities from highly contaminated areas by geogenic or geogenic-anthropogenic sources of contamination
Chronic risk estimate for soil contamination

## Slide 11
Health risk estimate for chronic disease occurrence due to soil ingestion by child population of the Slovak Republic – MUNICIPALITIES
Main results: medium risk levels were documented only in 6 municipalities from highly contaminated area by geogenic or geogenic-anthropogenic sources of contamination
Chronic risk estimate for soil contamination

## Slide 12
Health risk estimate for carcinogenic disease occurrence due to groundwater ingestion by adult population of the Slovak Republic - MUNICIPALITIES
Cancer risk estimate for groundwater contamination
Main results: high to very high risk was defined for more than 300 municipalities, because of many samples with arsenic contents below the detection limit 0.0005 mg.l-1 (the exact contents are not known) the first 3 risk categories were unified into one category of low to medium risk

## Slide 13
Health risk estimate for carcinogenic disease occurrence due to soil ingestion by population (additive model) of the Slovak Republic - MUNICIPALITIES
Cancer risk estimate for soil contamination
Main results: medium to high risk was defined for about 150 municipalities located in areas with a.) historical minining activities with ore deposit occurence, b.) area with anthropogenic contamination (depositions due to As-rich coal burning by power plant)

## Slide 14
Conclusions
Presented approach of health risk estimate based on national and regional geochemical data represents a convenient tool for identification of risk areas,
It is easily comprehensible for decision makers and can serve as basis for future works focused on detail studies of health risks.
Increased risk levels, both for chronic as well as in case of arsenic also carcinogenic diseases were identified mainly in highly contaminated areas with dominant geogenic or geogenic-anthropogenic source of contamination (historical mining areas).
The results of health risk estimation indicate that arsenic and antimony pose the highest chronic risk in some areas in the case of groundwater as well as soils.
Health risk estimation for soil contamination has highlighted the significance of exposure through soil ingestion in case of child population while for adults it is negligible.

## Slide 15
Some additional remarks / uncertainties:
Expression of chronic risk estimate for groundwater and soil contamination in the form of maximum value of hazard quotient instead of summmary hazard index is probably more objective way how to define risk levels (in this way we exclude the case when sum of no or low risk values result in one high risk value).
So far realized medical – geochemical researches in some of highly contaminated areas confirmed the existence of risk in regions identified as risk areas through the approach of model quantification of health risk.
Advantage of this approach is fast, visual and comprehensible visualization of risk areas for decision makers, disadvantage of this approach lies in data interpolation – local contamination partially spread out into non-contaminated areas.
There is still need to identify potential health risks associated with other elements that are essential at certain levels but have negative health effects at excess or deficit contents (e.g. macro-elements - Ca, Mg; Zn, Se etc.).
This issue is dealed with within the running project „GEOHEALTH“ , for more information about the project please go to the website www.geology.sk/geohealth.

## Slide 16
THANK YOU FOR YOUR ATTENTION
Acknowledgement
This research has been performed within the project LIFE10 ENV/SK/000086
„The impact of geological environment on health status of residents of the Slovak Republic“
financially supported by the EU’s funding instrument for the environment – Life+ programme.